## Slide 1: Flow Chart Diagnosis
Is It Electric, Hydraulic Or Mechanical ?

## Slide 2
Operate function. Does it operate
Check emergency stop switches. Are any engaged/pushed in.
Check all fuses. Are any fuses open circuit
or appear to have heat stress.
Is solenoid/coil magnetizing.
(use a small metallic object eg. Screw driver,
o’ring pick, paper clip)
Check for voltage/circuit at solenoid using
“Hirschman” tester. Is there a circuit/voltage
at the solenoid coil.
Repair wiring or control circuit (switch or relay)
no
Reset
Replace faulty fuses
Fault is either hydraulic
or mechanical
Replace solenoid/coil
Yes
IS IT ELECTRICAL ?

## Slide 3
Operate function. Does it operate.
Check hydraulic oil level.
Is it low
Check electrical operation. Is it
operating correctly
Is there oil flow to the function
control valve
Flow test hydraulic pump and check for
Leaks at pump and hoses between
Check for hose rupture or
Blockage and repair as necessary
no
Top up level
Refer to electrical flow chart
Is there flow out of
the control valve
Replace
Valve
Replace
pump
Check flow at function
Motor/Actuator
Replace/repair as
necessary
yes
yes
IS IT HYDRAULIC ?

## Slide 4
Check electrical and hydraulic
operations. Are they operating
correctly
Check function motor or actuator
for external leakage. Are there any leaks
Check mechanical/physical
condition of function. Is it
Blocked, seized, severely
damaged etc
Repair/replace as required
Refer to relevant flow charts
Repair as required
yes
no
yes
no
no
yes
IS IT MECHANICAL ?