## Slide 1
Harvesting operation

## Slide 2: Mechanical harvesting

## Slide 3: What are we doing?
Machine harvesting of grapes is not an exact science nor is it necessarily complex.
It can be very easy or it can be very difficult to achieve a good result.
The important thing is to understand what you are trying to achieve, what adjustments are available and what impact those adjustments have.
Whatever you do MUST be done safely. ALWAYS follow safe working practices.

## Slide 4: What do we want?
The main outcomes of mechanical grape harvesting are:
    maximum fruit removal
    minimum vine damage
    minimum trellis and post damage
    minimum MOG (matter other than grape)
    optimum harvesting speed

## Slide 5: How do we get it?
Factors affecting these outcomes:
  picking head position (head centred)
  picking head speed
  picking rod gap (pinch)
  harvester ground speed
  picking head height
  conveyor speed
  fan speed
  picking rod spacing
  picking rod shape
  vine condition
  trellis condition
  vineyard row condition and terrain
  weather conditions and time of day
  grape variety

## Slide 6: Preparing the harvester
    centre the picking head within the machine as shown by TVM
    if the head is not in the centred then the rods will pick unevenly resulting in poor picking quality, excessive cane damage and trellis and post damage

## Slide 7: Preparing the harvester
    place rods in machine in accordance with manufacturers recommendations
    ensure only enough rods to cover the fruit zone
    place the lowest rod on the side of the highest catcher plate

## Slide 8: Preparing the harvester
rods should curve inwards going from the front to the rear and have a straight section of about 300 – 400mm then curve slightly outwards for the last 100mm or so (refer drawing)
rods should be horizontal with no twists
all rods should be in a straight line in the vertical plane (refer drawing)
closer rods spacing (around 80mm) may be an advantage for some varieties such as Chardonnay and Cabernet

## Slide 9: Set up and operation
At all times think about what you are trying to achieve and how you can achieve it
    different ideas on the most important factor eg fruit left behind, broken posts, MOG etc
    the operator must endeavour to achieve the best result in all aspects
    you will need to develop a trade-off between achieving all the desirable criteria as it is rarely possible to achieve the ‘perfect’ job
    speed is the least important factor
    get all the other factors as best you can then consider speed but remember that increasing the speed will affect the other factors

## Slide 10: Set up and operation
    rod gap (pinch) should be set according to the canopy width ie the width of the ‘woody’ part of the canopy – generally around 50 – 70mm
    if pinch is too wide there will be poor fruit removal and excessive cane and leaf damage
    if pinch is too narrow there will be excessive cordon damage and post damage
    we want to shake the cordon not hit the fruit!
most grapes are harvested with a picking head speed in the range 460 – 530rpm
start with a slower speed then increase slowly until all fruit is being removed then back off slightly from there

## Slide 11: Set up and operation
    conveyor speed will affect MOG removal as well as machine efficiency – generally best to run the belts fast to reduce the fruit content across the belt thus allowing the fans better access to MOG
    fans should be run only fast enough to effectively remove MOG – too fast will result in fruit and juice extraction

## Slide 13: Problems and hints
when it seems that the fruit just won’t come off and nothing seems to work try the following:
      observe and think about what’s happening
      try to pinpoint a possible cause
      maybe make a quantum change to one adjustment
      only change one thing at a time
      picking grapes is often about making considered compromises

## Slide 14
  old woody vines can be difficult – try:
    widening the vertical rod gaps in the vicinity of the woody arms
    closer gaps in the vicinity of the bunches
    adding a couple of rods lower on the trunk with a closer pinch
    with this configuration the picking head speed could be reduced
Problems and hints

## Slide 15
  It is sometimes helpful to operate the harvester with a slight incline from front to rear
  When picking vines with two fruit zones there can be wider gaps between the two sets of rods
  The rod shape could be altered to help improve picking around the posts – ie pick more with the rod tips. Remember that leaf and cane damage may increase
  Sometimes bunches may fall off in front of the harvester as a result of damage or necrosis. When this is a problem try:
    altering the rod shape to pick more with the tips and
    increase ground speed
Problems and hints

## Slide 16: SUMMARY
THINK ABOUT WHAT YOU ARE TRYING TO ACHIEVE
THINK ABOUT WHAT ADJUSTMENTS YOU HAVE
COMPROMISE IS INEVITABLE
GET TO KNOW THE MACHINE
IF IN DOUBT, ASK